.TOC
.STL AS Reference Manual
.TTL
DECUS C LANGUAGE SYSTEM
The AS Assembler
for the PDP-11
by
David G. Conroy
Edited by
Martin Minow








.INT
This document describes the AS assembler, used  to  compile  the
output of the Decus C compiler to PDP-11 object code.
.MID DECUS Structured Languages SIG
.MID Version of 1-Aug-80
.PAG
.MID Copyright (C) 1980, DECUS
.LIN
General permission  to  copy  or  modify,  but  not  for
profit,  is  hereby  granted,  provided  that  the above
copyright notice is included and reference made  to  the
fact that reproduction privileges were granted by DECUS.
.LIN
The information in this document is  subject  to  change
without   notice  and  should  not  be  construed  as  a
commitment by Digital Equipment Corporation or by DECUS.
.LIN
Neither Digital Equipment Corporation,  DECUS,  nor  the
authors   assume  any  responsibility  for  the  use  or
reliability of this document or the described software.
.LIN
This software is  made  available  without  any  support
whatsoever.     The    person    responsible    for   an
implementation of this system should expect to  have  to
understand  and  modify  the source code if any problems
are  encountered  in  implementing  or  maintaining  the
compiler or its run-time library.  The DECUS `Structqre`
Lajcuaces Special Inperest Grkqp' is the  primary  focus
for coimqnication among users of this software.
.LIN
UNIX is  a  trademark  of  Bell  Telephone  Laboratories.   RSX,
RSTS/E,  RT11  and  VMS  are  trademarks  of  Digital  Equipment
Corporation.
.CPT Introduction
.LIN
AS is a three pass assembler for the PDP-11 inpended for use  as
a  targat  assembler  for  compilers.  It lacks some of the more
esoteric assembler directives of the  standard  DEC  assemblers;
it  also  lacks  any  form  of macro facility.  However, it does
posess the ability to extend any  branch  instruction  which  is
unable  to  reach  its  target label into the appropriate branch
over a jump.
.LIN
The input syntax is, in general, similar in style  to  MACRO-11.
The  actual  details  have  in many cases been changed so that a
programme intended to be assembled with AS cannot  be  assembled
with  MACRO-11.   The  syntax  is  compatible  with  the Unix AS
assembler.
.CPT Usage
.LIN
Under RSX11M or RSX compatibility mode under VMS, AS is  invoked
from MCR as follows:
.MID AS [-b] [-d] [-g] [-l] [-n] file [file ...]
.BLN 0
Under RSX compatibility mode under  RSTS/E,  AS  is  invoked  as
follows:
.MID XAS [-b] [-d] [-g] [-l] [-n] file [file ...]
.BLN 0
Under RT11 compatibility mode under RSTS/E,  AS  is  invoked  as
follows:
.MID AS file,file=file[/ switches]
.BLN 0
Under RT11, AS is invoked as follows:
.SWT 1
                RUN AS
                AS> object,list=source[/ switches]

.BLN 0
In RSX mode, the specified files are  assembled  separately  and
the  object  code is placed in a file (on the same device and in
the same UIC) having the same name as the source file but with a
filetype  of  OBJ.  The default filetype for source files is .S.
Wildcard file names are permitted on native RSX11-M and  RSX11-M
compatibility  mode under VMS.  They are not permitted on RSTS/E
or RT11.
.LIN
In RT11 mode, only one file may be assembled and the object  and
list files may be explicitly named.  The default case:
.SWT 1
                AS file

.BLN0
is equivalent to
.SWT 1
                AS file=file
.BLN
The following switches are defined:
.SWT 1
            b   Causes the assembler to  flag  all  branches  that  were
                extended to jumps.

            d   Causes the assembler to delete  the  source  file  after
                assembly.  This option makes compiling C programmes much
                easier.  This option is turned off by errors.

            g   Causes all symbols which are undefined  at  the  end  of
                pass  1  to  be given the type undefined external;  this
                corresponds to the .ENABL GBL directive of MACRO-11.

            l   Causes the assembler to generate a listing  file.   This
                is  the only way to generate a listing file on RSX mode.
                It works on RT11 mode as well.

            n   Causes the assembler to produce no  object  file.   This
                option  is  primarily  used to prevent creating a lot of
                useless  object  files  when  debugging  the  assembler;
                however,  it  may  be  of  use when one wishes to simply
                check a file for errors.
.LIN
The object file is in standard DEC format.   AS  writes  a  full
symbol  table (including internal symbols) into the GSD records.
These symbols are almost useless because the DEC linkers discard
internal  symbols,  but  are  present  for the benefit of future
generations of debuggers.  Note that the RSX  compiler  produces
an object file in the format required by TKB.TSK, while the RT11
compiler produces an object file  int  the  format  required  by
LINK.SAV.
.LIN
The title of the object file is always  set  to  the  first  six
characters of the source file name.  This is of interest only to
people who load overlaid programmes off libraries.
.CPT Lexical Conventions
.LIN
Assembler tokens consist of  identifiers  (`symbols',  `names'),
constants and operators.
.HLV 1
Identifiers
.LIN
An identifier consists of a sequence of alphanumeric  characters
(including  the  period  `.',  the tilde `~', and the underscore
`_'), the first of which may not be  numeric.   Only  the  first
eight  characters  of  the  name  are significant;  the rest are
discarded.   Upper  and  lower  case  are  treated  identically.
Because  the DEC object file stores symbols in radix 50, the `_'
character is mapped to `.' in the symbol  table  while  the  `~'
character  is  mapped  to  `$'.   Global  symbols must be unique
within the first six characters.
.MID WARNING
.BLN
Note that the mapping of `_' to `.' is  an  incompatible  change
from previous versions of this assembler.
.HLV 1
Constants
.LIN
An octal constant is a sequence of  digits;   `8'  and  `9'  are
taken  to  have  octal  values  of  10  and  11.   The number is
truncated  to  16  bits  and  interpreted  in  two's  complement
notation.
.LIN
A decimal constant is a  sequence  of  digits  terminated  by  a
period.   The  magnitude of the constant should be representable
in 15 bits;  i.e., be less than 32,768.
.LIN
A single character constant consists of the single  quote  (`'')
followed  by  any  ASCII  character  (except  the newline).  The
constant's value is the code for the character  right  justified
in the word, with zeros on the left.
.HLV 1
Operators
.LIN
There are several single and multiple character operators;   see
section 6.1.
.HLV 1
Blanks and Tabs
.LIN
Blanks and tabs may be used freely between tokens, but  may  not
appear  within  identifiers.   A  blank  or a tab is required to
separate adjacent tokens not otherwise separated.
.HLV 1
Comments
.LIN
The character `/' introduces a comment,  which  continues  until
the end of line.  Comments are ignored by the assembler.
.CPT Programme Sections
.LIN
AS permits multiple programme sections  (PSECTS);   however,  it
does  not  allow  the attributes of the programme sections to be
specified.  All programme sections receive the  attributes  LOW,
NOLIB, CON, RW, REL, LCL and ISPACE.
.CPT The Location Counter
.LIN
The special symbol `.' is the location counter.   Its  value  is
the  offset  into  the current programme section of the start of
the statement in which it appears.  It may be assigned to,  with
the  restrictions that the assignment must not either change the
programme section or cause the value to decrease.
.CPT Statements
.LIN
A programme consists of a sequence of  statements  seperated  by
newline  or  semicolons.   There  are three kinds of statements;
null statements, assignment statements and keyword statements.
.LIN
Any statement may be preceeded by any number of labels.
.HLV 1
Labels
.LIN
A name label consists of  an  identifier  followed  by  a  colon
(`:').   The programme section and value of the label are set to
those of the location counter.  It is an error for the value  of
a label to change between pass 1 and pass2.
.LIN
A temporary label consists of a digit `0' to `9' followed  by  a
colon (`:').  Such a label serves to define temporary symbols of
the form `xf' and `xb', where `x' is the  digit  of  the  label.
References  of  the form `xf' refer to the first temporary label
`x:' forward from the reference;  those of the form  `xb'  refer
to  the  first temporary label `x:' backward from the reference.
Such labels tend to conserve both the symbol table space of  the
assembler and the inventive powers of the programmer.
.HLV 1
Null Statements
.LIN
A null statement is just an empty line (which  may  have  labels
and  be  followed by a comment).  Null statements are ignored by
the assembler.  Common examples of  null  statements  are  empty
lines or lines consisting of only a label.
.HLV 1
Assignment Statements
.LIN
An assignment statement consists of an identifier followed by an
equal  sign  (`=')  and  an expression.  The value and programme
section of the identifier are set to  that  of  the  expression.
Any  symbol defined by an assignment statement may be redefined,
either by another assignment statement or by a label.
.HLV 1
Expression Statements
.LIN
An expression statement consists of an arithmetic expression not
beginning  with  a keyword.  The assembler computes its (16 bit)
value and  places  it  in  the  output  stream  along  with  the
appropriate relocation.
.HLV 1
String Statements
.LIN
A (UNIX style) string statement generates a  sequence  of  bytes
containing ASCII characters.  It consists of a left string quote
`<' followed by a sequence of  ASCII  characters  not  including
newline  followed  by  a  right  string  quote  `>'.  Any of the
characters may be replaced by an escape sequence as follows:
.SWT 1
                \b      Backspace       (0010)
                \f      Formfeed        (0014)
                \n      Newline         (0012)
                \r      Carriage Return (0015)
                \t      Tab             (0011)
                \nnn    Octal value     (0nnn)
.BLN 1
These escape sequences may also be used in the .ASCII and .ASCIZ
keyword statements and in character constants.
.HLV 1
Keyword Statements
.LIN
Keyword statements are the most common type;  all of the machine
operations  and assembler pseudo operations are of this type.  A
keyword statement begins with one of the assembler's  predefined
keywords,  followed  by  any  operands required by that keyword.
All of the keywords and their required operands are described in
sections 7 and 8.
.CPT Expressions
.LIN
An expression is a sequence of symbols representing a value  and
a  programme  section.   Expressions are made up of identifiers,
constants, operators and brackets.  All  binary  operators  have
equal  precidence  and  are  executed  in a strict left to right
order (unless altered by brackets).
.HLV 1
Types
.LIN
Every expression has a type determined  by  its  operands.   The
types that will be met explicitly are:
.SWT2
            Undefined

                Upon first  encounter,  each  symbol  is  undefined.   A
                symbol may also become undefined if it is assigned to an
                undefined expression.  It is an  error  to  assemble  an
                undefined  expression in pass 2.  Pass 1 allows assembly
                of undefined expressions, but phase errors may result if
                undefined  expressions  are  used  in  certain  contexts
                (i.e., in a .BLKW or .BLKB).


            Absolute

                An absolute symbol is  one  defined  untimately  from  a
                constant  or  from  the  difference  of  two relocatable
                values.


            Register

                Register symbols refer to the general registers  of  the
                PDP-11.   They  are  required  to  distinguish  register
                addressing from normal memory addressing.   The  symbols
                R0,  R1,  R2,  R3,  R4,  R5, SP and PC are predefined as
                register symbols.


            Relocatable

                All other user symbols are relocatable symbols  in  some
                programme   section.    Each   programme  section  is  a
                different relocatable type.
.LIN
Each keyword in the assembler has a secret type which identifies
it internally.  However, all of these secret types are converted
to absolute in expressions.  Thus any keyword may be used in  an
expression  to  obtain  the  basic  value  of that keyword.  For
machine operations the basic value is the opcode with all of the
bits  set  to  zero;   the  basic  value  of  pseudo
operations is, in general, uninteresting.
.HLV 1
Operators
.SWT 2
        The operators are:

                `+'             Addition
                `-'             Subtraction
                `*'             Multiplication
                `%'             Integer (truncating) division
                `&'             Bitwise AND
                `|'             Bitwise OR
                `>>'            Arithmetic right shift
                `<<'            Arithmetic left shift
                `-'             Unary negation
                `!'             Unary ones complement
                `^'             Value of the left, type of the right
.LIN 1
Expressions may be grouped by means of square brackets (`['  and
`]');  parentheses are reserved for use in address expressions.
.HLV 1
Type Propagation in Expressions
.LIN
When operands are combined in expressions the resulting type  is
a  function  of both the types of the operands and the operator.
Only  the  `+'  and  binary   `-'   operators   can   manipulate
non-absolute operands.
.LIN
The `+' operand permits the addition of  two  absolute  operands
(yielding an absolute result) and the addition of an absolute to
a non-absolute operand (yielding a result with the same type  as
the  non-absolute operand).  As a consequence, R3 may be refered
to as R0+3.
.LIN
The binary `-' operator permits two operands of the  same  type,
including  relocatable,  to  be subtracted (yielding an absolute
result) and an absolute to be  subtracted  from  a  non-absolute
(yielding  a  result  with  the  same  type  as the non absolute
operand).
.LIN
The notion of `complex relocation' is not supported.
.CPT Pseudo Operations
.LIN
The keywords listed below introduce  statements  which  generate
data or effect the later operation of the assembler.
.HLV 1
 .BYTE expression [ , expression ] ...
.LIN
The expressions in the comma separated list are truncated  to  8
bits  and  are assembled into successive bytes.  The expressions
must be absolute.
.HLV 1
 .WORD expression [ , expression ] ...
.LIN
The expressions in the comma separated list are  assembled  into
successive words.
.HLV 1
 .ASCII string
.LIN
The first nonblank (or tab) character after the  .ascii  keyword
is  taken as a delimiter.  Successive characters from the string
are assembled into  successive  bytes  until  the  delimiter  is
encountered.
.HLV 1
 .ASCIZ string
.LIN
This pseudo operation is identical  to  .ASCII  except  that  it
appends a null byte to the end of the string.
.HLV 1
 .EVEN
.LIN
If the location counter is odd, output a null byte so  the  next
statement will be assembled on an even boundry.
.HLV1
 .ODD
.LIN
If the location counter is even, assemble a null  byte  so  that
the next statement will be assembled on an odd boundry.
.HLV 1
 .BLKB expression
.LIN
This  statement  assembles  into  expression  null  bytes.   The
expression must be absolute.
.HLV 1
 .BLKW expression
.LIN
This  statement  assembles  into  expression  null  words.   The
expression must be absolute.
.HLV 1
 .GLOBL identifier [ , identifier ] ...
.LIN
The identifiers in  the  comma  separated  list  are  marked  as
global.  If they are defined in the current assembly they may be
referenced by other object modules;  if they are undefined  they
must be resolved by the loader before execution.
.HLV 1
 .ENTRY expresion
.LIN
The value of the expression becomes the transfer address of  the
object  file.   This  provides  the function of the label on the .END
statement in MACRO-11.
.HLV 1
 .PSECT identifier
.LIN
This statement switches the assembler to the specified programme
section.   If  the  programme  section  has not been encountered
previously `.' is set to 0;  otherwise it is set to the  highest
location  already assembled into that programme section.  .PSECT
attributes can not be defined.
.HLV 1
 .LIMIT
.LIN
This statement assembles into two words that are filled in  with
program  limit  information  by the linker.  When the program is
executed, the first word will have the  lowest  address  in  the
load  image and the second word will have the highest address in
the load image.
.HLV 1
 .FLT2	number [ , number ] ...
.LIN
The floating point numbers  in  the  comma  separated  list  are
converted  to  single  precision  floating  point binary and are
assembled into successive two word blocks.
.HLV 1
 .FLT4	number [ , number ] ...
.LIN
The floating point numbers  in  the  comma  separated  list  are
converted  to  double  precision  floating  point binary and are
assembled into successive four word blocks.
.HLV 1
End of file
.LIN
The assembly source is terminated by the end of the input  file.
There is no seperate .END statement.  
.CPT Machine Instructions
.LIN
Because of the rather  complicated  instruction  and  addressing
structure  of the PDP-11, the syntax of the machine instructions
is varied.  The PDP-11 handbooks should  be  consulted  for  the
detailed semantics of the instructions.
.HLV 1
Sources and Destinations
.LIN
The syntax of general source and destination  addresses  is  the
same  as  in  MACRO-11, except that `$' has been substituted for
`#' and `*' has been substituted for `@'.
.HLV 1
Simple Machine Instructions
.SWT1
        The following simple machine instructions are defined:

                HALT                    WAIT
                RTI                     BPT
                IOT                     RESET
                RTT                     CLC
                CLV                     CLZ
                CLN                     SEC
                SEV                     SEZ
                SEN                     CLE     (= CLC)
                SEE     (= SEC)
.LIN 1
The PDP-11 hardware allows  more  than  one  of  the  `set'  and
`clear' instructions to be ored together.  There is no syntactic
provision for this;  such instructions may be generated by means
of the .WORD pseudo operation.
.HLV 1
Branches
.LIN
The following instructions take an  expression  as  an  operand.
The  expression  must  lie in the same programme section as `.'.
If the value of the expression differs from the current location
by  more than 254 (decimal) bytes the instruction assembles as a
branch  to  .+6  having  the  opposite  sense   to   the   coded
instruction, followed by a jump to the desired location.
.SWT 1
                BR                      BNE
                BEQ                     BPL
                BMI                     BVS
                BVC                     BCS
                BCC                     BES     (= BCS)
                BEC     (= BCC)         BLT
                BGT                     BGE
                BLE                     BHI
                BLOS                    BHIS
                BLO 


.HLV 1
Single Operand Instructions
.LIN
The following single operand instructions take  one  address  of
the general source-destination type.
.SWT 1
                CLR                     CLRB
                COM                     COMB
                INC                     INCB
                DEC                     DECB
                NEG                     NEGB
                TST                     TSTB
                ASR                     ASRB
                ASL                     ASLB
                ROR                     RORB
                ROL                     ROLB
                ADC                     ADCB
                SBC                     SBCB
                JMP                     SWAB
                SXT

.HLV 1
Double Operand Instructions
.LIN
The   double   operand    instructions    take    two    general
source-destination type address fields, separated by a comma.
.SWT 1
                MOV                     MOVB
                CMP                     CMPB
                BIT                     BITB
                BIS                     BISB
                BIC                     BICB
                ADD                     SUB


.HLV 1
Other Instructions
.LIN
The following instructions have a more specialised syntax.  Here
reg  specifies  a  register  expression,  src  and  dst  general
source-destination addresses, and expr an expression.
.SWT 1
                JSR     reg,dst 
                RTS     reg
                CALL    dst             (same as JSR PC,dst)
                CALLR   dst             (same as JMP dst)
                RETURN                  (same as RTS PC)
                EMT     expr
                TRAP    expr
                SYS     expr            (same as EMT expr)
                ASH     src,reg
                ASHC    src,reg
                MUL     src,reg
                DIV     src,reg
                XOR     reg,dst
                MARK    expr
                SOB     reg,expr

.LIN 1
The expression in a SOB must be in the same programme section as
`.' and must be within 176 bytes of `.'.  The assembler does not
attempt to adjust SOB's which cannot  reach  their  destinations
into  DEC  and  BNE,  because  the  DEC  and  BNE do not set the
condition codes in the same manner.
.HLV 1
Floating Point Instructions
.LIN
The following floating  point  instructions  are  defined,  with
syntax as indicated.
.SWT 1
                ABSF    dst             ABSD    dst
                ADDF    src,reg         ADDD    src,reg
                CLRF    dst             CLRD    dst
                CMPF    reg,dst         CMPD    reg,dst
                DIVF    src,reg         DIVD    src,reg
                LDCDF   src,reg         LDCFD   src,reg
                LDCIF   src,reg         LDCID   src,reg
                LDCLF   src,reg         LDCLD   src,reg
                LDEXP   src             LDFPS   src
                LDF     src,reg         LDD     src,reg
                MODF    src,reg         MODD    src,reg
                MULF    src,reg         MULD    src,reg
                NEGF    dst             NEGD    dst
                STCFD   reg,dst         STCDF   reg,dst
                STCFI   reg,dst         STCDI   reg,dst
                STCFL   reg,dst         STCDL   reg,dst
                STEXP   dst             STFPS   dst
                STF     reg,dst         STD     reg,dst
                SUBF    src,reg         SUBD    src,reg
                SETF                    SETD
                SETI                    SETL
                STST    dst             CFCC
                TSTF    dst             TSTD    dst
.CPT Diagnostics
.LIN
Syntactic or semantic errors  in  the  source  are  reported  by
displaying  the  offending line on the console device, preceeded
by the appropriate error flags.  The name of the  file  is  also
displayed.
.SWT 1
                a               Addressing
                b               Byte allignment
                d               Illegal operation on `.'
                e               Expression syntax
                j               Jump (-b)
                m               Multiple definition
                o               Illegal operation code
                p               Phase
                q               Questionable syntax
                r               Relocation
                u               Undefined symbol
.LIN
Errors encountered in the accessing  of  files  or  in  internal
assembler  operations  are  reported  in  English on the console
device.  Overflows are fatal and require that the  assembler  be
modified to have a larger table (this is easy).
.LIN
The only really cryptic diagnostic is `AS>',  which  means  that
the  MCR  command line could not be obtained (you probably typed
RUN AS).  Type the command line you  would  have  typed  at  MCR
(including the leading AS).
.CPT Shortcomings and Caveats
.LIN
The assembler has some limitations.  Some of the more  important
ones  are listed below, and are classified as H (hard to fix), L
(likely to remain), F (fixable, and likely to be  fixed)  and  G
(go away).
.SWT 1
                F       No conditional assembly
                L       No macro facilities

.CPT Installation Notes
.LIN
The AS assembler may be installed on RSTS/E (V7.0 or  later)  in
RSX  or  RT11  modes, on RSX11M (V3.2 or later), on RT11 (V3B or
later), or on VMS  compatiblity  mode.   This  section  contains
installation instructions for RSTS/E and VMS.
.HLV 1
Installation on RSTS/E
.LIN
The AS assembler is installed after building the CC compiler  as
it  must  refer  to  the compiler support library which is built
together with CC.  Assuming the AS modules are stored in account
[5,3], the following command files should be run by ATPK:
.SWT 1
                XMAKAS          Make RSX-style assembler
                RMAKAS          Make RT11-style assembler
.LIN 1
You will have to edit the various command files as needed.
.LIN 0
In order to use AS, the System Manager must add the following to
the startup command file:
.SWT 1
                RUN $UTILTY
                ADD LOGICAL [5,2] C
                CCL XAS-=C:AS.TSK;0
                CCL AS-=C:AS.SAV;8192
                EXIT
.LIN 1
Note that the  RSX-style  assembler  must  run  from  a  defined
command.
.HLV 1
Installation on VMS
.LIN 1
The build command file  for  the  AS  assembler  is  VMAKAS.COM,
located in the same directory as other compiler components.  You
will have to edit it  as  needed,  running  it  as  an  indirect
command file.
.LIN 1
To use the assembler, define it as a command as follows:
.SWT 1
                XAS :== $device:[account]XAS.EXE XAS
.HLV 1
Installation on RT11
.LIN 1
After building the CC  compiler,  the  TMAKAS.COM  command  file
should be edited and executed.
.HLV 1
Installation on RSX-11M
.LIN 1
After building the CC  compiler,  the  MMAKAS.CMD  command  file
should be invoked.